## Slide 1
Prometheus Team
Measuring & Analysing Race Data
Diomataris Markos
National and Technical University
Of Athens
School of Electrical
and Computer Engineering
Notes: ΕΘΝΙΚΟ ΜΕΤΣΟΒΙΟ ΠΟΛΥΤΕΧΝΕΙΟ

## Slide 2
Goal
Better understanding of vehicle’s behaviour in race conditions.
Design the best on track strategy possible
Generate vehicle model

## Slide 3
Requirements
We wanted a system the measures and logs data:
What data?
Motor’s input electric power
Current Rms
Location

## Slide 4
Wattmeter 1 : i1 (v1 - v3)
Wattmeter 2 : i2 (v2 – v3)
W1 + W2 = ... = i1v1 + i2v2 - (i1 + i2) v3
(Kirchoff’s law, i1 + i2 + i3 = 0 => i1 + i2 = -i3)
W1 + W2 = i1v1 + i2v2 + i3v3 = Total instantaneous watts.
Measuring Power on a 3-phase Motor

## Slide 5
System overview
i1
i2
v1
v2
Storage
Real-time on-board signal processing
@10 Hz
@2.5 kHz
GPS
Data/Display Management
Lcd display

## Slide 6
Data processing
1. Noise rejection.
2. Automatic lap counting.
3. Automatic data mapping.
4. Visualisation of results.

## Slide 7
Round evaluation
Correlation between consumption and race condition factors (e.g. driver’s psychology)

## Slide 8
Current Variance / point
Useful conclusions
Localization of the most inconsistent (in the driving sense) part of the track using the motor’s current variance at each pont of the track throughout the race